## Slide 1
Professor Po-Tsang Huang
International College of Semiconductor Technology
National Yang Ming Chiao Tung University
Exercise 2
Supplement
Digital IC Design

## Slide 2: Construct a 4-bit Adder by verilog
In this exercise, TA will provide a RTL code of 4-bit adder.
Verify the behavior.
  Write a Testbnech to check.
(or used the Testbench provided by TA)
Verify in Behavior level:
Command: irun TESTBED_Adder_4bit.v -define RTL -debug -notimingchecks

## Slide 3: Synthesis
Synthesis: (covert to gate level)
Command: dc_shell-t -f syn.tcl | tee syn.log
(Used the .tcl provided by TA and modify the path in .tcl)
Verify in Gate level:
Commandirun irun TESTBED_Adder_4bit.v -define GATE -debug -v /path of NLDM/NLDM/Verilog/asap7sc7p5t_SIMPLE_RVT_TT_08302018.v /path of NLDM/NLDM/Verilog/asap7sc7p5t_SEQ_RVT_TT_08302018.v /path of NLDM/NLDM/Verilog/asap7sc7p5t_INVBUF_RVT_TT_08302018.v -nontcglitch
Synthesis the 4-bit adder.
Verify 4-bit adder in the gate level.

## Slide 4: Convert to SPICE Netlist
Convert to SPICE Netlist:
Step1. convert .v to .sp  command: ./Verilog2Spice
Strp2. add the VSS & VDD pin  command: python3.8 pin_adder_VSS_VDD.py
**** Input Vector ****
.VEC 'pattern_adder_4bit.vec‘
**** include the Adder****
.include ‘Adder_4bit_SYN_new.sp'
You need to generate the input Vector file for HSPICE simulation
.sp is the SPICE netlist you converted above
Convert the gate level 4-bit adder to spice.
Measure the delay & power of 4-bit adder by Hspice.